## Slide 1: StO corp- lotus effect facade coatings Name : sakthi Darshini.v register no : 192512024
BTA0179 BIOLOGY AND ENVIRONMENTAL SCIENCE FOR ENGINEERS

## Slide 2: INTRODUCTION
Nature has many self-cleaning surfaces — the best example is the lotus leaf.
The Lotus Effect refers to the leaf’s ability to repel water and dirt, staying clean even in muddy water.
Sto Corp developed Lotus-Effect coatings for building facades, inspired by this property.
These coatings make surfaces superhydrophobic and low maintenance.

## Slide 3: OBJECTIVE
To study and demonstrate the Lotus Effect.
To simulate a hydrophobic coating for building surfaces.
To compare plain vs. coated surfaces using contact angle measurement.
To understand how biomimicry and nanotechnology are used in real-life applications.

## Slide 4: CONCEPT OF LOTUS EFFECT
The lotus leaf surface has microscopic bumps (micro/nano structures).
It is covered with a waxy layer that repels water.
When water falls, it forms round droplets that roll off easily.
As droplets roll, they pick up dirt particles, creating a self-cleaning effect.

## Slide 5: PRINCIPLE & MECHANISM
The property behind this is super hydrophobicity.
A surface is called superhydrophobic when the contact angle >150°.
Two key factors:
1. Surface roughness (micro/nano texture)
2. Low surface energy (due to wax or fluoropolymers)
Combined, they cause non-wettability and self-cleaning action.

## Slide 6: MATERIALS AND METHODOLOGY
Materials Used:
Chart paper, glass tile/acrylic piece
Candle or wax
Water dropper
protractor (to measure contact angle)
Hydrophobic spray
Procedure:
1. Prepare two surfaces – one plain, one coated
2. Drop water on both.
3. Observe droplet behavior.
4. Measure contact angle and record observations.

## Slide 7: OBSERVATION AND RESULT
Surface type | observation | Contact angle | Result
Plain surface | Water spreads | 70 | hydrophillic
Coated surface | Water rolls off | 150 | superhydrophobic

## Slide 8: APPLICATIONS
Building and glass facades
Solar panels
Car windshields
Textiles and paints
Tiles and ceramics
Outdoor advertisements and signs

## Slide 9: ADVANTAGES AND LIMITATION
Advantages:
Self-cleaning and low maintenance
Water and dust repellent
Long-lasting, UV resistant
Reduces cleaning cost
Limitations:
Expensive coating materials
Skilled application required
Effect reduces over time with wear

## Slide 10: CONCLUSION
The Lotus Effect demonstrates how nature inspires modern technology.
Sto Corp’s coating replicates this effect to make facades self-cleaning and durable.
This project proved that superhydrophobic coatings can significantly reduce maintenance and improve building aesthetics.

## Slide 11: ENGINEERING STANDARDS
ASTM D7334 – Contact Angle Measurement Used to measure the hydrophobicity of coated surfaces. It confirms the Lotus Effect by ensuring the contact angle is above 150° (superhydrophobic surface).
ISO 2409 – Cross-Cut Adhesion Test Ensures strong bonding of the coating to building surfaces like glass, tiles, or masonry.
ASTM D6578 – Cleanability of Coated Surfaces Tests how easily dirt or dust can be removed, proving the self-cleaning property.
ISO 9227 – Salt Spray Test Checks the coating’s durability and resistance to corrosion and weathering in outdoor environments.
ISO 14001 – Environmental Management Standard Ensures the coating process is eco-friendly, safe, and meets environmental protection requirements.

## Slide 12: REFRENCES
1. Barthlott W., & Neinhuis C. (1997). Purity of the Sacred Lotus – Self-Cleaning Properties of Biological Surfaces. Planta, 202, 1–8.
2. Nosonovsky, M., & Bhushan, B. (2009). Superhydrophobic Surfaces and Emerging Applications. Springer.
3. Sto Corp. (2024). Lotusan Self-Cleaning Facade Coating Technical Data Sheet. Retrieved from www.stocorp.com
4. Zhang, X., Shi, F., & Noga, K. (2016). Design of Superhydrophobic Surfaces for Architectural Applications. Surface Engineering Journal, 32(4), 221–233.
5. ASTM D7334-08 (2013). Standard Practice for Contact Angle Measurement. ASTM International.